## Slide 1: Network Device Driver
Presented by : Vishal Wagh

## Slide 2: Content :
Detecting the device
Enabling the device
Understanding the network device
Bus-independent device access
Understanding the PCI configuration space
Initializing net_device
Understanding RealTek8139's transmission mechanism
Understanding RealTek8139's receiving mechanism
Making the device ready to transmit packets
Making the device ready to receive packets

## Slide 3: Detecting the device :
As a first step, we need to detect the device.
begin or continue searching for a PCI device by vendor/device id
struct pci_dev * pci_find_device (unsigned int vendor, unsigned int device, const struct pci_dev * from);
  vendor
  PCI vendor id to match.
  device
  PCI device id to match.
  from
  Previous PCI device found in search, or NULL for new search.

## Slide 4: Detecting the device :
#define VENDER_ID 0x1234
#define DEVICE_ID 0x5678
#include <linux/pci.h>
struct pci_dev *dev;
dev = pci_find_device(VENDER_ID, DEVICE_ID, NULL);
if (dev == NULL) {
printk(KERN_INFO "PCI device not found\n");
return -1; }
else{
printk(KERN_INFO "PCI device found\n");
}

## Slide 5: Enabling the device :
After detecting the device, we need to enable the device.
pci_enable_device — Initialize device before it's used by a driver.
int pci_enable_device (struct pci_dev * dev);
  struct pci_dev * dev
  PCI device to be initialized

## Slide 6: Enabling the device :
ret = pci_enable_device(dev);
if (ret != 0)
{
printk(KERN_INFO "Failed to enable device\n");
return ret;
}
else
{
printk(KERN_INFO "Enable device\n");
}

## Slide 7: Understanding struct net_device :
struct net_device {
char *name;
unsigned long base_addr;
unsigned char addr_len;
unsigned char dev_addr[MAX_ADDR_LEN];
unsigned char broadcast[MAX_ADDR_LEN];
unsigned short hard_header_len;
unsigned char irq;
void *priv;
};

## Slide 8
name - The name of the device. If the first character of the name is null, then register_netdev assigns it the name.
base_addr - The I/O base address.
addr_len - Hardware address (MAC address) length.
dev_addr - Hardware address (Ethernet address or MAC address)
broadcast - device broadcast address.
hard_header_len - The "hardware header length" is the number of octets that lead the transmitted packet before IP header, or other protocol information.
irq - The assigned interrupt number.
priv - Private data to the driver.

## Slide 11: This work is licensed under a Creative Commons Attribution-ShareAlike 3.0 Unported License. It makes use of the works of Kelly Loves Whales and Nick Merritt.